I got the modification information on the TS-2000 from reliable sources recently. The info. seems to be correct. My TS-2000 (K-type) worked.

- Remove the top and bottom cover.

- Loosen the 4 screws that tighen the front panel.

- Pull the front panel forward, holding the upper part.

- You will see a fan on the left.

- At the bottom right of the fan, there are jumpers.

- Remove R52 to expand the RX frequency.

- Remove R53 to expand the TX frequency.

- Remove R54 to expand the features.
(Cross-band Repeat, SkyCommand, External Remote and etc.)

R52 and R54 have been already removed on my transceiver.

After the modification, it transmits:
1.705 - 30MHz, 49-54MHz, 142-152MHz, 420-450MHz.

* It does not expand too much, though :-(

Oh, I forgot one important thing.
You must perform ALL RESET by pressing and hold [A=B] key when you turn on the transceiver. (You will lose all the memory data).