Remove top and bottom Covers an the Handle.

Remove the 4 screws (2 on each side) holding front panel at the main chassis.

Carefully remove the 4 Connectors to the main Unit.

Remove the metal cover upon the logic Unit (5 screws).

WARNING: The Diodes are not in the correct order (1-9) like in the IC-7700/7800 !!!

You will find the Diodes at the right Corner of the Circuit Board near the Processor Chip and VFO-Knob.

-----Left-----    -----Right----- >>PCB-End

IMS0 D68 RT50     D59 TXF0 -->remove

IMS1 D67 DLTX     D58 TXF1 -->remove

IMS2 D66 MTON     D57 TXF2 -->remove

IMS4 D64 -EMER    D55 RXF0

IMS3 D65 -KANA    D56 TXF3 -->remove

IMS7 D61 +        D52 RXF3

IMS6 D62 +        D53 RXF2

IMS8 D60 +        D51 TFRA

IMS5 D63 PAL      D54 RXF1

In the EU-Version all Diodes except D64 and D65 are fitted.

> For full TX-Coverage remove D56, D57, D58 and D59.

> For full RX-Coverage remove D52, D53, D54 and D55.

D51 must be always mounted.

No reset is necessary.